PRODUCT INFORMATION

BGU SERIES: Barrier Gate Operators

Model BGU barrier gates can be used for parking applications and revenue control. Through switch selections, the gate operator is universal and suitable for all installation and operational functions. Switch selection allows for full flexibility as to how and when the arm comes down in traffic control situations. Features Power on/off switch Duplex receptacle (115 VAC units only) Three-button control station included Accessory connections are 24-volt AC or DC Easily adjustable cam-operated limit switches Motor has manually-resettable overload Full system capable for access control and reversing devices White or yellow powdercoat finish - specify YS for Yellow; WS for White Options Stainless steel cabinet for installations in areas where high concentration of corrosive material is present Thermostatically-controlled strip heater Arm light kit BGU SERIES Models MODEL HP VOLTAGE & PHASE ARM SIZE APPLICATION BGU-10-311 1/3 115-1 10 FT. Parking applications and provisions for single-button, detector, radio, and 3-button controls, 24VAC accessories BGU-12-311 12 FT. BGU-14-311 14 FT. BGU-10-221 1/2 230-1 10 FT. BGU-12-221 12 FT. BGU-14-221 14 FT.

Specifications subject to change without notice.