PRODUCT INFORMATION

### GSX1000 SERIES: GateStar 1000 1/2 HP Extra Heavy-Duty Slide Gate Operator

GSX1000 SERIES Models - GateStar 1000 1/2 HP extra heavy-duty slide gate operator series, available in various supply voltages and options. Features Welded Uni-body frame #40 Drive chain on standard speed (25 ft. included) #50 Drive chain on high speed (25 ft. included) Architecturally designed, long-life cover Heavy, key-locked steel cover High efficiency, non-slip belt drive 1/2 HP instant-reverse, 3-wire motor Electronic dynamic braking DC solenoid actuated lock mechanism Solid-state circuitry and motor control with diagnostic LED readout Overload sensing system Built-in auto close timer Pre-wired loop detector sockets (two provided) MVP "smart" radio receiver with FC antenna Standard speed UL Listed for UL 325 (Classs I-IV) for U.S. and Canada High speed UL Listed for UL 325 (Class IV) for U.S. and Canada Options Drop out lock (unlocked power off) #50 Roller chain SPS-50 Standby power supply

| GateStar 1000 Models |
| --- |
| MODEL | HP | VOLTAGE & PHASE | MAXIMUM GATE WEIGHT | MAXIMUM GATE LENGTH | GATE SPEED |
| GSX1000 5011 | 1/2 | 115V 1P | 1575 LBS. | 45 FT. | 12"/second |
| GSX1000 5011-HS |  |  | 800 LBS. | 25 FT. | 24"/second |
| GSX1000 5021 | 1/2 | 230V 1P | 1575 LBS. | 45 FT. | 12"/second |
| GSX1000 5021-HS |  |  | 800 LBS. | 25 FT. | 24"/second |