PRODUCT INFORMATION

LPX1000 SERIES: Leader Plus 1/2 HP Heavy-Duty Slide Gate Operator

LPX1000 SERIES - Leader Plus 1/2 HP heavy-duty slide gate operator series, available in 115-volt and 230-volt supply voltages and options. Features Welded heavy-duty frame #41 Drive chain (25 ft. included) Architecturally designed, long-life cover Heavy duty 10:1 gear reducer allows emergency manual operation without tools Fail secure lock standard (gate locks when power off) Electronic dynamic braking Built-in auto close timer Overload sensing system MVP "smart" radio receiver with FC antenna Built-in operator lock Built-in maximum run timer Built-in master/second capability Solid-state circuitry with diagnostic LED readout UL Listed for UL 325 (Class I-IV) for U.S. and Canada (120 VAC only) -HS (Class III-IV only) -230V LPX1000 not listed Options Fail safe lock (unlocked power off) #50 Roller chain SPS-50 Standby power supply LEADER PLUS Models MODEL HP VOLTAGE & PHASE MAXIMUM GATE WEIGHT MAXIMUM GATE LENGTH GATE SPEED LPX1000 5011 1/2 115V 1P 1300 LBS. 35 FT. 12"/second LPX1000 5011-HS 1000 LBS. 18"/second LPX1000 5021 1/2 230V 1P 1300 LBS. 35 FT. 12"/second

Specifications subject to change without notice